## Slide 1: Transistor Bias Circuits

## Slide 2: Objectives
Discuss the concept of dc biasing of a transistor for linear operation
Analyze voltage-divider bias, base bias, and collector-feedback bias circuits.
Basic troubleshooting for transistor bias circuits

## Slide 3: Introduction
For the transistor to properly operate it must be biased.
There are several methods to establish the DC operating point.
We will discuss some of the methods used for biasing transistors.

## Slide 4: Biasing
Biasing: The DC voltages applied to a transistor in order to turn it on so that it can amplify the AC signal.
The term biasing is an all-inclusive term for the application of dc voltages to establish a fixed level of current and voltage.
For transistor amplifiers the resulting dc current and voltage establish an operating point, Since the operating point is a fixed point on the characteristics, it is also called the quiescent point (abbreviated Q-point).
DC Biasing – used to set the initial values of IB, IC, and VCE for ac operation of the transistor

## Slide 5: The DC Operating Point
The goal of amplification in most cases is to increase the amplitude of an ac signal without altering it.
Notes: Fig 5-1a, b, & c

## Slide 6: The DC Operating Point
For a transistor circuit to amplify it must be properly biased with dc voltages. The dc operating point between saturation and cutoff is called the Q-point. The goal is to set the Q-point such that that it does not go into saturation or cutoff when an a ac signal is applied.
Notes: Fig 5-2a & Fig 5-4

## Slide 7: The DC Operating Point
With the dc load line superimposed across the collector curves for this particular transistor we see that 30 mA of collector current is best for maximum amplification, giving equal amount above and below the Q-point. Note that this is three different scenarios of collector current being viewed simultaneously.
Notes: Fig 5-2a & Fig 5-4

## Slide 8: The DC Operating Point
Amplification process:
Notes: Fig 5-5 circuit and load line w/signals

## Slide 10: Voltage-Divider Bias
Voltage-divider bias is the most widely used type of bias circuit. Only one power supply is needed and voltage-divider bias is more stable(independent) than other bias types. For this reason it will be the primary focus for study.
Notes: Fig 5-9 Voltage-Div. Bias

## Slide 11: Voltage-Divider Bias
Apply your knowledge of voltage-dividers to understand how R1 and R2 are used to provide the needed voltage to point A(base). The resistance to ground from the base is not significant enough to consider in most cases. Remember, the basic operation of the transistor has not changed.
Notes: Fig 5-9 Voltage-Div. Bias

## Slide 12: Voltage-Divider Bias
In the case where base to ground resistance(input resistance) is low enough to consider, we can determine it by the simplified equation RIN(base) = DCRE
We can view the voltage at point A of the circuit in two ways, with or without the input resistance(point A to ground) considered.
Notes: Fig 5-10a & b

## Slide 13: Voltage-Divider Bias
For this circuit we will not take the input resistance into consideration. Essentially we are determining the voltage across R2(VB) by the proportional method.
VB = (R2/(R1 + R2))VCC
Notes: Fig 5-9 Voltage-Div. Bias

## Slide 14: Voltage-Divider Bias
We now take the known base voltage and subtract VBE to find out what is dropped across RE. Knowing the voltage across RE we can apply Ohm’s law to determine the current in the collector-emitter side of the circuit. Remember the current in the base-emitter circuit is much smaller, so much in fact we can for all practical purposes we say that IE approximately equals IC.
IE ≌ IC
Notes: Fig 5-9 Voltage-Div. Bias

## Slide 15: Voltage-Divider Bias
Although we have used npn transistors for most of this discussion. There is basically no difference in it’s operation with exception to biasing polarities. Analysis for each part of the circuit is no different than npn transistors.
Notes: Fig 2-16

## Slide 16: Base Bias
We used base bias type circuit for the purpose of simplicity for the initial discussion of transistor circuits. This type of circuit is very unstable since it’s  changes with temperature and collector current. Try Exercise 5.6
Notes: Fig 5-19 Base bias circuit

## Slide 17: Example
Assume that RB=240kohm, RC==2.2kohm, Vcc=12
IBQ=(Vcc-VBE)/RB = 47.08microA
ICQ=ß IBQ = 2.35mA
VCEQ=Vcc-ICQRC=6.83V
VB=VBE=0.7V
VC? What is Ic(sat)?
Notes: Fig 5-19 Base bias circuit

## Slide 18: Emitter Bias
This type of circuit is independent of  making it as stable as the voltage-divider type. The drawback is that it requires two power supplies.
Two key equations for analysis of this type of bias circuit are shown below. With these two currents known we can apply Ohm’s law and Kirchoff’s law to solve for the voltages. Try Exercise 5.7
IC ≌ IE and IC= IB* 
IB ≌ IE/
≌(-VEE-VBE)/(RE + RB/DC)‏
Notes: Fig 5-21a npn emitter bias

## Slide 19: Collector-Feedback Bias
Collector-feedback bias is kept stable with negative feedback, although it is not as stable as voltage-divider or emitter. With increases of IC, less voltage is applied to the base. With less IB ,IC comes down as well. The two key formulas are shown below. Try Exercise 5.8
IB = (VC – VBE)/RB
IC = (VCC - VBE )/ (RC + RB/DC ) assuming IC is much bigger than IB
Notes: Fig 5-23 collector feedback

## Slide 20: Summary
The purpose of biasing is to establish a stable operating point (Q-point).
The Q-point is the best point for operation of a transistor for a given collector current.
The dc load line helps to establish the Q-point for a given collector current.
The linear region of a transistor is the region of operation within saturation and cutoff.

## Slide 21: Summary
Voltage-divider bias is most widely used because it is stable and uses only one voltage supply
Base bias is very unstable because it is  dependant.
Emitter bias is stable but require two voltage supplies.
Collector-back is relatively stable when compared to base bias, but not as stable as voltage-divider bias.

## Slide 22: 4. BJT AS AN AMPLIFIER

## Slide 23: Basic BJT Amplifiers Circuits
Single-Stage BJT Amplifiers
C-E Amplifiers
To operate as an amplifier, the BJT must be biased to operate in active mode and then superimpose a small voltage signal vbe to the base.
DC + small signal
coupling capacitor
(only passes ac signals)

## Slide 24: Basic BJT Amplifiers Circuits
Single-Stage C-E BJT Amplifiers

## Slide 25: Basic BJT Amplifiers Circuits
vBE=vi+VBE
Apply a small signal input voltage and see ib
Single-Stage C-E BJT Amplifiers

## Slide 26: Basic BJT Amplifiers Circuits
vi = 0  IB、IC、VCE
vo out of phase with vi
iC=ic+IC
vCE=vce+VCE
See how ib translates into vce.
Single-Stage C-E BJT Amplifiers

## Slide 27: 5. BJT AS A SWITCH

## Slide 28: 5. BJT AS A SWITCH
A transistor when used as a switch is simply being biased so that it is in:
    cutoff (switched off)
    saturation (switched on)
Notes: Fig 4-22

## Slide 29: Conditions in Cutoff
Conditions in Saturation
Since VCE(sat) is very small compared to
VCC, it can be neglected.
Neglect leakage current and all currents
are zero. BE junction is reverse biased.
5. BJT AS A SWITCH

## Slide 30: Example 3
For the transistor circuit in below figure, what is VCE when VIN=0v?
What minimum value of IB is required to saturate this transistor if βDC is 200?
Calculate the maximum value of RB when VIN=5V.

## Slide 31: Solution Example 3
When VIN=0V, the transistor is in cutoff (act as open switch), so VCE(cutoff)=VCC = 10V.
Since VCE(sat) is neglected (assumed 0V),
This is the value of IB necessary to drive transistor to point of saturation.
c) When transistor is ON, VBE=0.7V. The voltage across RB is
VRB=VIN – VBE = 5 – 0.7 = 4.3V
By Ohm’s Law, the maximum value of RB is: