## Slide 1: TCP / IP Protocol Suite
Prof. Dr. Md Zahidul Islam

## Slide 2
PROTOCOLS
AND
STANDARDS
1.2

## Slide 3: Protocols
Syntax
Semantics
Timing

## Slide 4: Standards
De facto: e.g., TCP/IP
De jure: e.g., ISO OSI

## Slide 5
STANDARDS
ORGANIZATIONS
1.3

## Slide 6
Standards Creation Committees
International Standards Organization (ISO)
International Telecommunications Union–
Telecommunication Standards Sector (ITU-T)
Institute of Electrical and Electronics Engineers (IEEE)
Electronic Industries Association (EIA)
American National Standards Institute (ANSI)

## Slide 7
Forums
Regulatory Agencies
Frame Relay Forum
ATM Forum
Federal Communications Commission (FCC)
National Communications Commission (NCC)

## Slide 8
The websites for the above organizations are given in Appendix G.

## Slide 9
INTERNET
STANDARDS
1.4

## Slide 10
Figure 1-2
Maturity levels of an RFC

## Slide 11
Figure 1-3
Requirement levels of an RFC

## Slide 12
Chapter 2
The OSI Model and
TCP/IP
Protocol Suite

## Slide 13
CONTENTS
THE OSI MODEL
LAYERS IN THE OSI MODEL
TCP/IP PROTOCOL SUITE
ADDRESSING
TCP/IP VERSIONS

## Slide 14
THE
OSI
MODEL
2.1

## Slide 15
ISO is the organization. OSI is the model.

## Slide 16
Headers are added to the data at layers 6, 5, 4, 3, and 2. Trailers are usually added only at layer 2.

## Slide 17
Figure 2-3
An exchange using the OSI model

## Slide 18
Figure 2-8
End-to-end delivery

## Slide 19
Figure 2-10
Reliable end-to-end delivery of a message

## Slide 20
Figure 2-14
Summary of layers

## Slide 21
TCP/IP
PROTOCOL
SUITE
2.3

## Slide 22
Figure 2-15
TCP/IP and OSI model

## Slide 23
ADDRESSING
2.4

## Slide 24
Figure 2-16
Addresses in TCP/IP

## Slide 25
Figure 2-17
Relation-
ship
of
layers
and
addresses
in TCP/IP

## Slide 26
Example 1
Figure 2.18 shows an example of physical addresses.

## Slide 27
Figure 2-18
Physical addresses

## Slide 28
Example 2
Most local area networks use a 48-bit (6 bytes) physical address written as 12 hexadecimal digits, with every 2 bytes separated by a hyphen as shown below:
07-01-02-01-2C-4B
A 6-byte (12 hexadecimal digits) physical address

## Slide 29
Example 3
Figure 2.19 shows an example of Internet addresses.

## Slide 30
Figure 2-19
IP addresses
Note the changes in physical address!!

## Slide 31
Example 4
As we will see in Chapter 4, an Internet address (in IPv4) is 32 bits in length, normally written as four decimal numbers, with each number representing 1 byte. The numbers are separated by a dot. Below is an example of such an address.
132.24.75.9

## Slide 32
Example 5
Figure 2.20 shows an example of transport layer communication.

## Slide 33
Figure 2-20
Port addresses

## Slide 34
Example 6
As we will see in Chapters 11 and 12, a port address is a 16-bit address represented by one decimal number as shown below.
753 A 16-bit port address

## Slide 35
TCP/IP
VERSIONS
2.5

## Slide 36
Versions:
Version 4 (current): 32-bit IP address
Version 5
Version 6 (in promotion): 128-bit IP address

## Slide 37
Chapter 4
IP Addresses:
Classful Addressing

## Slide 38
CONTENTS
INTRODUCTION
CLASSFUL ADDRESSING
OTHER ISSUES
A SAMPLE INTERNET

## Slide 39
INTRODUCTION
4.1

## Slide 40
An IP address is a 32-bit address.

## Slide 41
The IP addresses are unique.
One IP address points to one computer.
But a computer may have many IP addresses.

## Slide 42
Address Space
addr15
addr1
addr2
addr41
addr31
addr226
…………..
…………..
…………..
…………..
…………..
…………..
…………..

## Slide 43
RULE:
addr15
addr1
addr2
addr41
addr31
addr226
…………..
…………..
…………..
…………..
…………..
…………..
…………..
If a protocol uses N bits to
define an address,
the address space is 2N
because each bit can have two
different values (0 and 1)
and N bits can have 2N values.

## Slide 44
The address space of IPv4 is
232 or 4,294,967,296.

## Slide 45
01110101 10010101 00011101 11101010
Binary Notation

## Slide 46
Figure 4-1
Dotted-decimal notation

## Slide 47
0111 0101 1001 0101 0001 1101 1110 1010
Hexadecimal Notation
75 95 1D EA
0x75951DEA

## Slide 48
The binary, decimal, and hexadecimal number systems are reviewed in Appendix B.

## Slide 49
Example 1
Change the following IP address from binary notation to dotted-decimal notation.
10000001 00001011 00001011 11101111
Solution
129.11.11.239

## Slide 50
Example 2
Change the following IP address from dotted-decimal notation to binary notation.
111.56.45.78
Solution
01101111 00111000 00101101 01001110

## Slide 51
Example 3
Find the error, if any, in the following IP address:
111.56.045.78
Solution
There are no leading zeroes in
dotted-decimal notation (045).

## Slide 52
Example 3 (continued)
Find the error, if any, in the following IP address:
75.45.301.14
Solution
In dotted-decimal notation,
each number is less than or
equal to 255; 301 is outside this range.

## Slide 53
Example 4
Change the following IP addresses from binary notation to hexadecimal notation.
10000001 00001011 00001011 11101111
Solution
0X810B0BEF or 810B0BEF16

## Slide 54
CLASSFUL
ADDRESSING
4.2

## Slide 55
Figure 4-2
Occupation of the address space
231(50%)
228(6.25%)
229(12.5%)
230(25%)

## Slide 56
In classful addressing, the address space is divided into five classes: A, B, C, D, and E.

## Slide 57
Figure 4-3
Finding the class in binary notation

## Slide 58
Figure 4-4
Finding the address class

## Slide 59
Example 5
How can we prove that we have 2,147,483,648 addresses in class A?
Solution
In class A, only 1 bit defines the class.
The remaining 31 bits are available
for the address. With 31 bits,
we can have 231 or 2,147,483,648 addresses.

## Slide 60
Example 6
Find the class of the address:
00000001 00001011 00001011 11101111
Solution
The first bit is 0. This is a class A address.

## Slide 61
Example 6 (Continued)
Find the class of the address:
11000001 10000011 00011011 11111111
Solution
The first 2 bits are 1; the third bit is 0.
This is a class C address.

## Slide 62
Figure 4-5
Finding the class in decimal notation

## Slide 63
Example 7
Find the class of the address:
227.12.14.87
Solution
The first byte is 227 (between 224 and 239);
the class is D.

## Slide 64
Example 7 (Continued)
Find the class of the address:
193.14.56.22
Solution
The first byte is 193 (between 192 and 223);
the class is C.

## Slide 65
Example 8
In Example 4 we showed that class A has 231 (2,147,483,648) addresses. How can we prove this same fact using dotted-decimal notation?
Solution
The addresses in class A range from 0.0.0.0 to
127.255.255.255. We notice that we are
dealing with base 256 numbers here.

## Slide 66
Solution (Continued)
Each byte in the notation has a weight.
The weights are as follows:
2563 , 2562, 2561, 2560
Last address: 127 × 2563 + 255 × 2562 + 255 × 2561 + 255 × 2560 = 2,147,483,647
First address: = 0
If we subtract the first from the
last and add 1, we get 2,147,483,648.

## Slide 67
Network identity (network ID) is a portion of the TCP/IP address that is used to identify individuals or devices on a network such as a local area network or the Internet. ... A network ID is also known as network identification or NetID.

## Slide 68
Figure 4-6
Netid and hostid

## Slide 69
Figure 4-7
Blocks in class A

## Slide 70
Millions of class A addresses are wasted.

## Slide 71
Figure 4-8
Blocks in class B

## Slide 72
Many class B addresses are wasted.

## Slide 73
Figure 4-9
Blocks in class C

## Slide 74
The number of addresses in a class C block is smaller than the needs of most organizations.

## Slide 75
Class D addresses are used for multicasting; there is only one block in this class.

## Slide 76
Class E addresses are reserved for special purposes; most of the block is wasted.

## Slide 77
Network Addresses
The network address is the first address.
The network address defines the network to the rest of the Internet.
Given the network address, we can find the class of the address, the block, and the range of the addresses in the block

## Slide 78
In classful addressing, the network address (the first address in the block) is the one that is assigned to the organization.

## Slide 79
Example 9
Given the network address 17.0.0.0, find the class, the block, and the range of the addresses.
Solution
The class is A because the first byte is between
0 and 127. The block has a netid of 17.
The addresses range from 17.0.0.0 to
17.255.255.255.

## Slide 80
Example 10
Given the network address 132.21.0.0, find the class, the block, and the range of the addresses.
Solution
The class is B because the first byte is between
128 and 191. The block has a netid of
132.21. The addresses range from
132.21.0.0 to 132.21.255.255.

## Slide 81
Example 11
Given the network address 220.34.76.0, find the class, the block, and the range of the addresses.
Solution
The class is C because the first byte is between
192 and 223. The block has a netid of 220.34.76.
The addresses range from 220.34.76.0
to 220.34.76.255.

## Slide 82
Mask
A mask is a 32-bit binary number that gives the first address in the block (the network address) when bitwise ANDed with an address in the block.

## Slide 83
Figure 4-10
Masking concept

## Slide 84
Figure 4-11
AND operation

## Slide 85
The network address is the beginning address of each block. It can be found by applying the default mask to any of the addresses in the block (including itself). It retains the netid of the block and sets the hostid to zero.

## Slide 86: Default Masks
Class | Mask in Binary | Mask in dotted-decimal
A | 11111111 0…0 | 255.0.0.0
B | 11111111 11111111 0…0 | 255.255.0.0
C | 1…1 00000000 | 255.255.255.0

## Slide 87
Example 12
Given the address 23.56.7.91 and the default class A mask, find the beginning address (network address).
Solution
The default mask is 255.0.0.0, which means
that only the first byte is preserved
and the other 3 bytes are set to 0s.
The network address is 23.0.0.0.

## Slide 88
Example 13
Given the address 132.6.17.85 and the default class B mask, find the beginning address (network address).
Solution
The default mask is 255.255.0.0, which means
that the first 2 bytes are preserved
and the other 2 bytes are set to 0s.
The network address is 132.6.0.0.

## Slide 89
Example 14
Given the address 201.180.56.5 and the class C default mask, find the beginning address (network address).
Solution
The default mask is 255.255.255.0,
which means that the first 3 bytes are
preserved and the last byte is set to 0.
The network address is 201.180.56.0.

## Slide 90
We must not apply the default mask of one class to an address belonging to another class.

## Slide 91
CIDR (Classless Inter-Domain Routing) Notation
18.46.74.10/8
141.24.74.69/16
200.14.70.22/24
Number of 1’s in the mask
Address Depletion
We have run out of class A and B addresses, and a class C block is too small for most middle-sized organizations.

## Slide 92
OTHER
ISSUES
4.13

## Slide 93
Figure 4-12
Multihomed devices

## Slide 94: Location, Not Names
An internet address defines the network location of a device, not its identify.
Movement of computer from one network to another means that its IP address must be changed.
Flat addressing vs. hierarchical addressing

## Slide 95: Special Addresses
Special Address | Netid | Hostid | Source or Destination
Network address | Specific | All 0s | None
Direct broadcast address | Specific | All 1s | Destination
Limited broadcast address | All 1s | All 1s | Destination
The host on this network | All 0s | All 0s | Source
Specific host on this network | All 0s | Specific | Destination
Loopback address | 127 | Any | Destination

## Slide 96
Figure 4-13
Network addresses

## Slide 97
Figure 4-14
Example of direct broadcast address

## Slide 98
Figure 4-15
Example of limited broadcast address

## Slide 99
Figure 4-16
Example of this host on this address

## Slide 100
Figure 4-17
Example of specific host on this network

## Slide 101
Figure 4-18
Example of loopback address

## Slide 102
Private Addresses
A number of blocks in each class are assigned for private use. They are not recognized globally. These blocks are depicted in Table 4.4
Class | Netids | Blocks
A | 10.0.0 | 1
B | 172.16 to 172.31 | 16
C | 192.168.0 to 192.168.255 | 256

## Slide 103
Unicast, Multicast, and Broadcast Addresses
Unicast communication is one-to-one.
Multicast communication is one-to-many.
Broadcast communication is one-to-all.

## Slide 104
Multicast delivery will be discussed in depth in Chapter 15.